## Slide 1
Compressor Performance Map Prediction using Machine Learning Algorithms: A multi-map training approach
Heba Youssef, Amanda Pieyre, and Ahmed Jhinaoui
Propulsion and Space Research Center, Technology Innovation Institute, Abu Dhabi, UAE
ISABE 2026 | Youssef, Pieyre & Jhinaoui | Technology Innovation Institute
Notes: • Welcome, name + TII
• co-authors: Amanda Pieyre, Ahmed Jhinaoui
• topic: reconstructing missing compressor map regions with ML

## Slide 2: About us
Advanced Technology Research Council
Business development
Research & development
Commercialization
TII: 9 research centers, +1100 employees
Advanced Materials
AI and Digital Science
Autonomous Robotics
Cryptography
Directed Energy
Propulsion and Space
Quantum
Renewable and Sustainable Energy
Secure Systems
Heba Youssef
Researcher Jet Engine Digital Twins
Amanda Pieyre
Lead Researcher Engine Performance
Ahmed Jhinaoui
Lead Data Scientist
Digital Engineering
Notes: • TII = research pillar of ATRC (ASPIRE / TII / VentureOne)
• 9 research centres; we are Propulsion & Space
• introduce co-authors + roles

## Slide 3: Compressor maps are key for performance modelling
Needed for
Off-design performance
Transient simulation
Control development
But are rarely complete
Full maps are proprietary
Rig tests and CFD are costly
Sparse data near surge and choke
Notes: • what a map is: Wc vs Rc, one line per speed, efficiency contours
• choke side = vertical end, surge side = stability limit
• needed for: off-design, transients, control
• but: proprietary, costly to test, sparse near surge/choke
• → we work with incomplete maps

## Slide 4: What this work adds: a configurable framework
Prediction using Machine Learning [1–5]
One fixed model
Prediction for that map only
This work: configurable framework
Support maps
Target map
Support maps
…
3 nearest
…
β
…
arc length
…
Features
…
shape
…
Model
…
ExtraTrees
…
Selected options from each policy
reconstructed target
Single map
+
one map · fills gaps between known points · single output Rc, with Wc assumed known → data leakage [5]
multi-output: Wc, Rc, ηc
[1] Ghorbanian & Gholamrezaei 2009 [2] Yu et al. 2007 [3] Ying et al. 2020 [4] Zhong et al. 2023 [5] Ibrahim et al. 2024 (our previous work)
Notes: • previous ML work: one map, one fixed model, gaps between known points
• usually Rc only → Wc assumed known = leakage
• our approach: support maps + incomplete target
• pick one option per policy, per missing-data case
• output: complete missing region, Wc AND Rc, plus efficiency

## Slide 5: Seven missing-data cases
Missing speed line
Intermediate
Lower exterior
Upper exterior
visible
hidden: never used in training, baseline prediction, or input features creation
Missing region of one speed line
Choke end
Surge end
Completely missing boundary region
Full choke
Full surge
Notes: • 7 controlled cases on Acp_4001; purple = hidden
• family 1: whole speed line (intermediate / lower / upper)
• family 2: choke or surge end of ONE line
• family 3: whole boundary, all lines
• hidden points never used anywhere

## Slide 6: A configurable framework: one option from each policy
Selected for each missing-data case and prediction target (Wc–Rc geometry or ηc surface)
Support maps
Target only
1 map
3 nearest
5 nearest
All
β definition
Uniform
Arc length
Mass-flow progress
Bend anchored
Endpoint step
Feature set
Shape
Direction
Full
Model
Linear
Ridge
ExtraTrees
Random Forest
Gradient Boosting
GPR
+ hyperparameter selection per model
Notes: • for each case + target quantity, pick one option per policy
• support maps: none → all
• β definition: 5 options
• feature set: shape / direction / full
• model + hyperparameters
• → not one universal model

## Slide 7: Prediction workflow
1
Baseline
from visible data
2
Support maps
ranked by similarity
3
β coordinate
Map data point position
4
Features
input sets
5
Models
+ tuning
6
Geometry prediction
Wc, Rc
(speed line shape)
7
Efficiency prediction
ηc
(surface contours)
8
Evaluation
configuration selection
Policy selection
customizable per missing data case
Notes: • roadmap for the rest of the talk
• 1 baseline → 2-5 policy selection (customisable)
• 6 geometry = speed-line shape (Wc, Rc)
• 7 efficiency = surface / contours
• 8 evaluation + configuration choice

## Slide 8: Predict baseline first, then learn only the correction
Baseline
›
Support maps
›
β coordinate
›
Features
›
Models
›
Geometry
›
Efficiency
›
Evaluation
Model target: residual learning
ΔWc,z = (Wc − Wc,0) / σW,vis
ΔRc,z = (Rc − Rc,0) / σR,vis
Wc,0, Rc,0: baseline values
σvis: standard deviations calculated from the visible points
z: standardised quantity
Chart: Wc
| 1.7610399999999999 | 1.7610399999999999 | 1.7610399999999999 | 1.7610399999999999 | 1.7608699999999999 | 1.7582100000000001 | 1.7571399999999999 | 1.7545500000000001 | 1.75065 | 1.7441599999999999 | 1.7305200000000001 | 1.70455 | 1.6692899999999999 | 1.6259699999999999 | 1.58117 | 1.53664 | 1.49397 | 1.4522299999999999 | 1.4114100000000001 | 1.3715200000000001
v2 | 2.6806 | 2.8018 | 2.923 | 3.0442 | 3.1651 | 3.281 | 3.3999 | 3.5155 | 3.628 | 3.7344 | 3.8243 | 3.8847 | 3.9213 | 3.9362 | 3.9442 | 3.9492 | 3.9552 | 3.9599 | 3.9634 | 3.9658
v4 | 4.3576 | 4.52 | 4.6823 | 4.8446 | 5.0069 | 5.1693 | 5.3322 | 5.4939 | 5.6509 | 5.7939 | 5.914 | 6.0245 | 6.1123 | 6.1917 | 6.2529 | 6.3096 | 6.3613 | 6.404 | 6.4397 | 6.4572
original speed
missing speed
baseline: linear interpolation
residual learned by the model
Nc = 80%
Nc = 95%
Nc = 90%
Prediction = baseline + residual
Notes: • example: 90% line hidden between visible 80% and 95%
• baseline = linear interpolation in speed, point by point
• outer lines → extrapolation; surge/choke → extend local direction
• grey = hidden truth
• model learns only the residual (standardised)
• prediction = baseline + residual

## Slide 9: Where the maps come from
Baseline
›
Support maps
›
β coordinate
›
Features
›
Models
›
Geometry
›
Efficiency
›
Evaluation
GasTurb
component map collection, maps from open literature
8 radial maps
1 target + 7 candidate support maps
20
points per speed line, 1300 points in total
Acp_4001
target map and case study (AGARD CP 400)
Candidate support maps
ASME-94-GT-73
Pep82r15
Rad1kg
RadComp9-AIAA-79-1159
RadComp10-AIAA-79-1159
T100rad
T800_c
Different sizes and operating ranges, which is why every map is normalized separately
Notes: • maps from GasTurb collection, open-literature sources
• 8 radial maps: 1 target + 7 support
• 20 points per line, 1300 points
• Acp_4001 = target, used throughout
• very different sizes → normalise each map

## Slide 10: Per-map normalization makes maps comparable
Baseline
›
Support maps
›
β coordinate
›
Features
›
Models
›
Geometry
›
Efficiency
›
Evaluation
Raw maps
Chart: Wc
Acp_4001 (target)
support maps
Per-map z-score
Chart: Wc,z
xz = (x − μx,vis) / σx,vis
μ, σ: mean and standard deviation of the visible points of that map
Notes: • raw maps: ranges differ by an order of magnitude
• z-score each map on its visible points
• after scaling the shapes overlap
• model learns scale-free corrections

## Slide 11: Support maps are ranked by similarity to the target
Baseline
›
Support maps
›
β coordinate
›
Features
›
Models
›
Geometry
›
Efficiency
›
Evaluation
Map descriptor
Number of speed lines
Speed range and spread
Normalised Wc, Rc and ηc spans
Mean slope and curvature of the speed lines
Chart: Descriptor distance to Acp_4001
| RadComp10 | T800_c | RadComp9 | T100rad | Pep82r15 | ASME-94-GT-73 | Rad1kg
Distance | 4.18 | 4.11 | 3.8 | 3.41 | 3.26 | 2.6 | 1.65
Policies tested
Target only
1 map
3 nearest
5 nearest
All maps
  Descriptors are standardized and maps are ranked by Euclidean distance to the target
Notes: • descriptor per map: lines, speed range/spread, spans, slope, curvature
• standardise descriptors, rank by distance to target
• 3 nearest here: Rad1kg, ASME-94-GT-73, Pep82r15
• full-region cases: descriptor from visible part only
• policies tested: target only → all maps

## Slide 12: β tells the model where a point sits on the speedline
Baseline
›
Support maps
›
β coordinate
›
Features
›
Models
›
Geometry
›
Efficiency
›
Evaluation
When we look at a map, we easily notice shapes, but a model mainly sees a numeric table.
To give the model info on map shape, we introduce β values.
β = position along the line
Example (a): β=0 at choke, and β=1 at surge, indicates missing point position
From visible data only
Computed on the baseline, so it exists when target points are hidden
5 possible definitions. Best definition is selected per missing data case
Notes: • we see shapes, the model sees numbers
• near surge/choke Rc(Wc) is multi-valued → need position along the line
• β = 0 at choke end, 1 at surge end
• computed from the visible baseline → available when points are missing
• 5 definitions, selected per case

## Slide 13: Input features
Baseline
›
Support maps
›
β coordinate
›
Features
›
Models
›
Geometry
›
Efficiency
›
Evaluation
Feature | Information given to the model | Shape | Direction
Nc,rel, Nc,z | Target speed relative to the visible speeds | ● | ●
β, β² + β(1−β) in Shape | Position along the predicted line | ● | ●
Wc,0,z, Rc,0,z | Baseline point before correction | ● | ●
W′0, R′0 | Local change along the baseline | ● | 
s0, κ0 | Local slope and curvature of the baseline | ● | 
Boundary point | Last visible point next to the gap |  | ●
Direction vector | Direction in which the line is extended |  | ●
Map descriptors | Spans of Wc, Rc, and Nc, and number of original speeds | only in the Full variant | 
Missing speed lines:
Shape 11 inputs
or
Full = Shape + 4 descriptors 15
Surge / choke completion:
Direction 10 inputs
or
Full = Direction + 4 descriptors 14
Notes: • all sets: target speed + β terms + baseline point
• shape set adds local derivatives, slope, curvature (11)
• direction set adds boundary point + extension direction (10)
• full = + 4 map descriptors (15 / 14)
• feature set is part of the per-case selection

## Slide 14: Candidate models and hyperparameter tuning
Baseline
›
Support maps
›
β coordinate
›
Features
›
Models
›
Geometry
›
Efficiency
›
Evaluation
Linear
Linear regression
Ridge
Tree ensembles
ExtraTrees
Random Forest
Gradient Boosting
Kernel
Gaussian process
Hyperparameters tuned per case
no. of trees
feature subsampling
leaf size
depth
learning rate
regularisation
kernel
Notes: • linear references vs tree ensembles vs kernel
• same model predicts both Wc and Rc residuals
• hyperparameters tuned per case
• training examples: hide known regions of training maps

## Slide 15: Efficiency: surface prediction allows using simpler methods
Baseline
›
Support maps
›
β coordinate
›
Features
›
Models
›
Geometry
›
Efficiency
›
Evaluation
Approach A
Common RBF surface
ηc = fRBF(Nc, β)
Visible target efficiency only: no baseline, no support maps
+ Simple, same set-up for all cases
+ Accurate when interpolating
− Extrapolates poorly when a boundary is missing
Approach B
Case-wise prediction
ηc = ηc,0 + residual
Same baseline and policy selection as in geometry prediction
+ Better when extrapolating
− Needs its own configuration per case
Notes: • efficiency is a smooth surface → simpler method can work
• A: RBF surface on visible efficiency only (no baseline, no support maps)
• A is good interpolating, poor when a boundary is missing
• B: case-wise = same baseline + policy selection as geometry
• efficiency paired with predicted geometry afterwards

## Slide 16: How errors are measured
Baseline
›
Support maps
›
β coordinate
›
Features
›
Models
›
Geometry
›
Efficiency
›
Evaluation
Geometry (Wc, Rc)
RMSE per withheld speed line or endpoint segment
Computed separately for Rc and Wc, then averaged per case
Ranking score:
    Sgeom = ½ (RMSERc + RMSEWc)
Efficiency (ηc)
RMSE per withheld speed line or endpoint segment
Only ηc, so nothing to combine; averaged per case
Ranking score:
    mean ηc RMSE
RMSE = √( mean (y − ŷ)² ) over the hidden points
Notes: • geometry: RMSE per withheld line/segment, Rc and Wc separately, averaged
• ranking score = mean of the two (ranking only)
• efficiency: single output → mean ηc RMSE is the score
• no hidden Wc used as input
• caveat: configurations ranked with the answer key → best case (see limitations)

## Slide 17
Results Acp_4001 case study
Notes: • results section: all on Acp_4001

## Slide 18: Wc and Rc prediction: all seven missing-data cases
Notes: • selected predictions, all seven cases
• black = hidden truth, dashed = baseline, red = prediction
• line cases overlay separate masking runs; full-region = one removal

## Slide 19: Wc and Rc prediction: one example per case
Median score is used to select the zoomed-in result for each missing-data case
Notes: • one representative example per case (median score = typical, not best)
• biggest correction: lower exterior line
• endpoint cases: small errors, visible part anchors the baseline

## Slide 20: Residual learning reduces geometry error in all cases
Chart: Rc RMSE
| Full surge region | Full choke region | Surge end of one line | Choke end of one line | Upper exterior speed line | Lower exterior speed line | Intermediate speed line
Predicted baseline | 0.0515 | 0.0093 | 0.0515 | 0.0093 | 0.1123 | 0.2975 | 0.1689
Selected configuration | 0.0229 | 0.005 | 0.0198 | 0.0037 | 0.0521 | 0.03 | 0.0643
Chart: Wc RMSE
| Full surge region | Full choke region | Surge end of one line | Choke end of one line | Upper exterior speed line | Lower exterior speed line | Intermediate speed line
Visible-data baseline | 0.0121 | 0.0037 | 0.0121 | 0.0037 | 0.0429 | 0.064 | 0.0344
Selected configuration | 0.0085 | 0.0017 | 0.0072 | 0.0015 | 0.0086 | 0.012 | 0.0176
−46 to 90%
Rc RMSE vs baseline
−30 to 81%
Wc RMSE vs baseline
Notes: • baseline vs selected configuration, per case
• Rc error down 46-90%, Wc down 30-81%
• largest gain lower exterior (0.30 → 0.03)
• smallest Wc gain: full surge region

## Slide 21: Best configuration selection depends on missing data case
Case | Support maps | β definition | Features | Model | ηc method
Intermediate speed line | All | Bend anchored | Full | ExtraTrees | RBF
Lower exterior speed line | 3 nearest | Uniform | Shape | ExtraTrees | Case-wise
Upper exterior speed line | 3 nearest | Mass-flow progress | Shape | ExtraTrees | Case-wise
Choke end of one line | 3 nearest | Endpoint step | Full | ExtraTrees | Case-wise
Surge end of one line | Target only | Endpoint step | Full | Linear | RBF
Full choke region | All | Endpoint step | Direction | Linear | Case-wise
Full surge region | 1 support map | Endpoint step | Full | ExtraTrees | Case-wise
Notes: • selected configuration differs per case
• intermediate uses all maps; exterior cases 3 nearest
• surge end of one line: target map only + linear regression
• ExtraTrees 5 cases, linear 2

## Slide 22: Efficiency results: reconstructed contours
Notes: • reconstructed efficiency contours, visible data + prediction
• red = predicted geometry, grey dashed = hidden
• contours stay smooth across all cases

## Slide 23: Efficiency prediction: one example per case
Median score is used to select the zoomed-in result for each missing-data case
Notes: • same zoomed view for efficiency: ηc vs Wc
• black = truth, red = prediction at its predicted Wc
• captures the drop towards choke

## Slide 24: Efficiency results: the best method depends on the case
Chart: ηc RMSE
| Full surge region | Full choke region | Surge end of one line | Choke end of one line | Upper exterior speed line | Lower exterior speed line | Intermediate speed line
Predicted baseline | 0.008 | 0.0106 | 0.008 | 0.0106 | 0.0147 | 0.0185 | 0.0087
RBF surface | 0.0141 | 0.0206 | 0.0025 | 0.0111 | 0.0134 | 0.0249 | 0.0046
Case-wise prediction | 0.004 | 0.002 | 0.0047 | 0.0023 | 0.0042 | 0.0105 | 0.0049
RBF surface is best:
when the gap lies between visible data: intermediate speed line, surge end of one line
Case-wise prediction is best:
when extrapolating: exterior speed lines and whole choke/surge regions
Notes: • RBF best where the gap sits between visible data (intermediate, surge end)
• case-wise best when extrapolating (exterior lines, whole boundaries)
• full choke: 0.021 → 0.002
• selected method below baseline in every case

## Slide 25: Summary
Visible target + support maps
Baseline
Policy selection: maps · β · features · model
Geometry Wc, Rc
Efficiency ηc
No leakage
hidden points are never used in training, baseline prediction, or input features creation
Residual correction works
Rc RMSE −46 to 90% Wc RMSE −30 to 81% vs baseline
No universal configuration
support maps, β, features and model depend on the case
Efficiency
RBF surface when interpolating, Case-wise prediction when extrapolating
Notes: • framework recap: inputs → baseline → policy selection → geometry → efficiency
• no leakage
• residual correction works in every case
• no universal configuration
• efficiency: simple when interpolating, case-wise when extrapolating

## Slide 26: Limitations and next steps
Limitations
Tested on radial compressor maps only
No explicit physical constraints near surge and choke
Next steps
More variations of compressor maps, including axial compressors
Physics constraints near surge and choke
Coherent geometry and efficiency reconstruction: ensuring continuity
Notes: • radial maps only
• automatic selection = recommendation, not guarantee
• no explicit physics constraints near surge/choke
• next: more maps incl. axial, physics constraints, geometry-efficiency coherence

## Slide 27
Thank you!
Happy to take your questions
Connect on LinkedIn
linkedin.com/in/heba-yy
ISABE 2026 | Youssef, Pieyre & Jhinaoui | Technology Innovation Institute
Notes: • thank you + questions
• QR = LinkedIn

## Slide 28
Appendix

## Slide 29: Appendix: geometry errors per case
Case | Rc baseline | Rc selected | Reduction | Wc baseline | Wc selected | Reduction
Intermediate speed line | 0.1689 | 0.0643 | 61.9% | 0.0344 | 0.0176 | 48.9%
Lower exterior speed line | 0.2975 | 0.0300 | 89.9% | 0.0640 | 0.0120 | 81.3%
Upper exterior speed line | 0.1123 | 0.0521 | 53.6% | 0.0429 | 0.0086 | 80.0%
Choke end of one line | 0.0093 | 0.0037 | 59.5% | 0.0037 | 0.0015 | 60.0%
Surge end of one line | 0.0515 | 0.0198 | 61.5% | 0.0121 | 0.0072 | 40.5%
Full choke region | 0.0093 | 0.0050 | 45.8% | 0.0037 | 0.0017 | 54.9%
Full surge region | 0.0515 | 0.0229 | 55.5% | 0.0121 | 0.0085 | 30.0%
Notes: • backup: per-case geometry errors and reductions

## Slide 30: Appendix: efficiency errors per case
Case | Visible baseline | RBF surface | Case-wise prediction | Selected
Intermediate speed line | 0.0087 | 0.0046 | 0.0049 | RBF
Lower exterior speed line | 0.0185 | 0.0249 | 0.0105 | Case-wise
Upper exterior speed line | 0.0147 | 0.0134 | 0.0042 | Case-wise
Choke end of one line | 0.0106 | 0.0111 | 0.0023 | Case-wise
Surge end of one line | 0.0080 | 0.0025 | 0.0047 | RBF
Full choke region | 0.0106 | 0.0206 | 0.0020 | Case-wise
Full surge region | 0.0080 | 0.0141 | 0.0040 | Case-wise
Notes: • backup: per-case efficiency errors, selected method

## Slide 31: Appendix: model comparison per case
Notes: • backup: model comparison per case

## Slide 32: Appendix: automated configuration selection
Case | Rc, picked with target truth | Rc, picked with support maps only | Wc, picked with target truth | Wc, picked with support maps only
Lower exterior speed line | 0.0300 | 0.0315 | 0.0120 | 0.0133
Intermediate speed line | 0.0643 | 0.0868 | 0.0176 | 0.0193
Upper exterior speed line | 0.0521 | 0.2603 | 0.0086 | 0.0267
Picked with target truth (paper results): every configuration is scored against the true values of the removed Acp_4001 points, and the best one is kept. Not possible for a real incomplete map, so this is a ideal case.
Picked with support maps only: the same kind of region is removed from each support map, where the true values are known. Configurations are scored there, and the winner is applied to Acp_4001.
Notes: • backup: picking the configuration with vs without the target truth